%%
%%                     NOBEYAMA98  ABSTRACT
%%
%%                  Deadline: September 5, 1998
%%
%%        Please send by E-MAIL to nbym98@solar.nro.nao.ac.jp.
%%

\documentstyle{article}
\textwidth 15 cm
\oddsidemargin 1 cm
\evensidemargin 1 cm
\textheight 24 cm
\topmargin 0 cm
\begin{document}

%% TITLE


\begin{center}
{\large\bf {Development of the Siberian Solar Radio Telescope}}
\end{center}

%%

\begin{center}
{\bf {V.~Zandanov, A.~Altyntsev, and S.~Lesovoi }}
\end{center}

%% INSTITUTIONS

\begin{center}
Institute of Solar-Terrestrial Physics, Irkutsk, Russia
\end{center}

%% ABSTRACT

The variety of generation mechanisms for radio emission and the
dependence of their efficiency on parameters of emitting electrons
makes the interpretation of observations difficult if spectral
data of high spatial resolution are absent. Also, the dynamic range of
solar phemomena is extremely wide. This is why a further development of
the SSRT is required towards the extension of both the dynamic and the
spectral range of observations.

The SSRT is a cross-shaped interferometer consisted of two 622~m long linear
antenna arrays in the E-W and the N-S directions, each of which consists of
128 antennas. In solar activity cycle~23, observations started at the SSRT
to provide with two-dimensional (2-D) solar maps at the frequency of 5.7~GHz at
within 3--5~min with a spatial resolution of down to $22^{\prime \prime}$.

Our proposal is to expand the SSRT to multi-frequency capability. It can
be achieved through the replacing of the existing in each dish narrow-band
feeds with composite multi-wave feeds to ensure the receiving of signals in
the range of 2--9.4~GHz, and through the equipping each antenna of the array
with modules for amplification and conversion of the UHF signal.

At the focus of each dish (paraboloid of 2.5~m diameter) will be placed
three incorporated feeds of V.N.~Dikiy design (St.~Petersburg State
Technical University) which are inserted into each other. The phase centers
of the three feeds can be easily brought into coincidence. The ranges
of the working frequencies are 2--4, 5.6--5.8, and 7.4--9.4~GHz,
respectively. The left- and right-hand circularly polarized components
of the emission received by the antenna pass from each feed to
the polarization modulators and then to low-noise 15~dB UHF
amplifiers with the input noise temperature of 50--60~K.

The UHF modules serve to separate a
discrete set of frequencies and to convert them to the frequency of
the SSRT waveguide line of 5.7~GHz. The signals of different frequency
channels will be received with temporal sharing.

A special advantage of the proposal is an almost total
utilization of the existing equipment of the SSRT: antennas, the complex
waveguide system with amplifiers, bridges and phase shifters,
and receiving systems.

The parameters of the proposed telescope should be following:
\begin{itemize}
\item Frequencies: 2.1, 3.9, 5.7, 7.5, and 9.3~GHz
\item Bandwidth of receivers: 100--200~MHz
\item Integration time for image synthesis: 0.16--0.3~s
\item Temporal resolution in the fast 1-D mode: 4~ms
\item Renewal time of 2-D map: down to 1~min
\item Renewal time of 1-D image: down to 20~ms
\item Flux sensitivity: a few Yan
\end{itemize}

The implementation of this program on the basis of the SSRT
will result in the creation of a substantially developed,
actually new, multi-wave instrument.

Together with the Nobeyama Radio Heliograph whose observational daytime
is almost the same, it promises significant progress in understanding
physics of solar activity. The high spatial and temporal
resolution data on bursts covering the layers from chromosphere up to
corona will essentially improve the forecasting geoefficiency of solar
events.

Part of this work was supported by the Russian projects of {\em RFFI}
No.~96-02-16648, No.~97-02-16906 and {\em  Astronomia}.


\end{document}