%%
%%                     NOBEYAMA98  ABSTRACT
%%
%%                  Deadline: September 5, 1998
%%
%%        Please send by E-MAIL to nbym98@solar.nro.nao.ac.jp.
%%

\documentstyle{article}
\textwidth 15 cm
\oddsidemargin 1 cm
\evensidemargin 1 cm
\textheight 24 cm
\topmargin 0 cm
\begin{document}

%% TITLE

\begin{center}
{\large\bf
{HESSI - A Mission for X-Ray and Gamma-Ray Imaging and Spectroscopy
 in MAX-2000}} \\
\end{center}

%% AUTHORS

\begin{center}
{\bf {G. J. Hurford$^{1}$ and the HESSI Team}}
\end{center}

%% INSTITUTIONS

\begin{center}
$^1$ {Space Sciences Laboratory, University of California, Berkeley} \\
{ c/o NASA/GSFC, Code 682, Greenbelt, MD 20771, USA} \\
\end{center}

%% ABSTRACT

The High Energy Solar Spectroscopic Imager (HESSI) is a NASA Small-
Explorer class mission to be launched in July 2000.  The primary
scientific objective is the study of particle acceleration and energy
release in flares.  Both the science goals and imaging technique have
close links to the objectives and methodology of solar radio
observations.  In the case of HESSI, a solar-pointed, rotating
spacecraft will carry a single instrument for high-resolution
imaging/spectroscopy from 3 kev through 20 MeV.  This energy range,
which includes the thermal and superthermal components, nonthermal x-
rays, nuclear lines and the high-energy gamma-ray continuum, will be
observed with a common set of 'optics' and detectors.  The instrument
uses a set of 9 rotating modulation collimators with FWHM angular
resolutions ranging from 2.3 arcseconds through 183 arcseconds.  Nine
germanium detectors will provide sufficiently high energy resolution
(~1 keV below 1 MeV, increasing to 5 keV at 20 MeV) to enable effective
interpretation of steep continuum spectra and to resolve most of the
nuclear gamma-ray lines.  Ground-based radio and optical observations
are considered an essential component of the mission.  Broad
participation in analysis of HESSI data will be encouraged by the
on-line, immediate and unrestricted availability of the HESSI database
and analysis software to the science community.  This paper will
outline the instrument design, status, calibration, and imaging
technique, and plans for the data analysis software.


\end{document}

%% End of NOBEYAMA98   ABSTRACT.