\documentstyle{article}
\textwidth 15 cm
\oddsidemargin 1 cm
\evensidemargin 1 cm
\textheight 24 cm
\topmargin 0 cm
\begin{document}

%% TITLE

\begin{center}
{\large\bf {Current-injection Model for Loop Flares\\
and Active Region Transient Loop Brightenings}}
 \end{center}

%% AUTHORS
\begin{center}
{\bf {T.Miyagoshi, Y.Uchida, T.Yabiku, and S Hirose}}
\end{center}

%% INSTITUTIONS

\begin{center}
{Dept. Physics, Science university of Tokyo}
\end{center}

%% ABSTRACT

    We think that active regions are higher in temperature (and
accordingly, in density) due to the presence of magnetic field. But
the important thing is not the simple presence of the field itself,
but the field into which the current is dynamically leaking in from
the part of the field imbedded in the convection-dominated
subphotospheric layer. The active region corona, in our view, is the
disposing place of such current, or packets of magnetic twists, that
can be created, transported, and destroyed magnetodynamically (NOT
like the static current in the so-called current circuit model), after
leaking out from the subphotospheric layers into the active region
corona along the flux tubes (Uchida et al.1998, Yabiku et al.1998).
    What, then, happens when such a leakage of the magnetic twist from
the subphotosphere to the outer layers (chromosphere and corona)?
When the twist (a large amplitude torsional Alfven wave) propagates
along the flux tube towards the photosphere, the twisted part will
emerge to the photosphere rather quickly due also to the magnetic
buoyancy of the twisted part, and comes out to the chromosphere-
corona. The toroidal and poloidal components that were far from the
force-free condition with high gas presure, now go into a new
equilibrium (force free state) generally through pinching, and this
successively occur along the flux tube dynamically as this finite
amplitude torsional Alfven wave propagates. This progressing pinching
sets the gas into a spinning hypersonic flow because the front
progresses with Alfven velocity.
   This may correspond to the jetting of the pinch-heated gas to be
identified with the active region transient loop brightening. If two
of them coming into a loop from both ends (namely, if the second one
comes into the loop within the propagation time of the first one), the
collision of those two hypersonic flows with fast and slow shocks will
occur at a high part of the loop, and a very high temperature region
(as high as $10^8 K$) will be resulted. We identify this with the super
high temperature region appearing at the start of a loop flare, with
the following phenomena, like the evaporation of the chromospheric gas
due to heat conduction etc. for the loop flares occurring as the
result of the appearance of the superhot region.
   Details of the 3D MHD simulation with the observed type of
dynamical distortion, confinement of the heated gas to the high part
of the loop, appearance of over-the-loop-top high temperature source,
etc. will be explained at the symposium.

\end{document}
%%End of NOBEYAMA98 ABSTRACT