%%
%%                     NOBEYAMA98  ABSTRACT
%%
%%                  Deadline: September 5, 1998
%%
%%        Please send by E-MAIL to nbym98@solar.nro.nao.ac.jp.
%%

\documentstyle{article}
\textwidth 15 cm
\oddsidemargin 1 cm
\evensidemargin 1 cm
\textheight 24 cm
\topmargin 0 cm
\begin{document}

%% TITLE

\begin{center}
{\large\bf { The structure of solar millimetre emission sources \\
derived from eclipse observations }}
\end{center}

%% AUTHORS

\begin{center}
{\bf {V. Nagnibeda$^{1}$ and B. Rozanov$^{2}$ }}
\end{center}

%% INSTITUTIONS

\begin{center}
$^1$ {St.Petersburg University Astronomical Institute, St.Petersburg, Russia} \\
$^2$ {Baumann Moscow State Technical University, Moscow, Russia} \\
\end{center}

%% ABSTRACT

The principal aim of solar eclipse radio observations is to obtain
high-resolution brightness distribution of sources on the solar disc and
the limb. This information can be derived from an eclipse curve, i.e.
from records of the solar signal as the solar disc is covered and uncovered
by the moon disc. At short millimetre wavelengths serious difficulties
exist: the strong influence of terrestrial atmosphere absorption and its
fluctuations as well as the low contrast of solar sources. In order to reduce
significancy these obstacles a special small expedition millimetre radio
telescope has been designed at Baumann Moscow State Technical University.
In this radio telescope a conic scanning by the antenna beam around the solar
disc center is used. Thus the quiet sun signal modulated by fluctuations
of the atmospheric attenuation is cancel out in the output signal and the
noise due to fluctuations of the atmospheric absorption is suppresseed and
the sensitivity to the eclipse signal is improved.

Several total solar eclipses were observsd with this radio telescope
at 3.4 mm wavelength. In this spectral range the active region emission
is due only to bremsstrahlung and it is important to reveal a fine structure
of AR emission ( the sunspot and the plage components) and to know whether
there is any difference between emission of these components. For some
sources in several eclipse observations a fine structure of active region
sources was not found out with spatial resolution of 5-10 arcsec, so
the sunspot-associated sources have brightness temperatures less than
20\% above the plage (the entire AR).

\end{document}

%% End of NOBEYAMA98  ABSTRACT.