%%
%%                     NOBEYAMA98  ABSTRACT 
%%
%%                  Deadline: September 5, 1998
%%  
%%        Please send by E-MAIL to nbym98@solar.nro.nao.ac.jp.
%% 

\documentstyle{article}
\textwidth 15 cm
\oddsidemargin 1 cm
\evensidemargin 1 cm
\textheight 24 cm
\topmargin 0 cm
\begin{document}

%% TITLE 

\begin{center}
{\large\bf { Geomagnetic disturbances around  the solar minimum of
cycle 22 and their solar sources}} 
\end{center}

%% AUTHORS 

\begin{center}
{\bf {Shinichi Watari$^{1}$ and Takashi Watanabe$^{2}$ }}
\end{center}

%% INSTITUTIONS

\begin{center}
$^1$ {Communications Research Laboratory, 4-2-1 Koganei,
Tokyo 184-8795, Japan} \\ 
$^2$ {Ibaraki University, 2-1-1 Bunkyo, Mito, Ibaraki 310-8512, Japan} \\
\end{center}

%% ABSTRACT
 % Please write your abstract here. Size limit is one page (15 cm x 24 cm)
 % with 10pt font size. Please avoid to use figures and to use \new...
 % and \renew... commands.

The Sun has been observed by the soft X-ray telescope on board {\it Yohkoh}
since September,1991.
This continuous observation from the space enable to detect signatures of
coronal holes and coronal mass ejections (CMEs).
The WIND satellite  has continuously observed solar wind since November, 1994.
This {\it in situ} observation also helps to detect interplanetary signatures
of coronal holes and CMEs.
Their observations well covered the solar minimum of cycle 22.
High-speed streams from coronal holes and CMEs play a major role
for interplanetary disturbances or geomagnetic disturbances.
Now, the solar sources of geomagnetic disturbances can be determined
more accurately than ever by using the solar observations from the space and
the {\it in situ} solar wind observations.

The solar sources of geomagnetic disturbances with Dst $\leq$ -50 nT were
examined.
There were still recurrent high-speed streams from the coronal holes
around the solar minimum of cycle 22.
Geomagnetic disturbances associated with CMEs were
sometimes observed in the high-speed streams.
CMEs were found in front of the high-speed streams,
in the high-speed streams, in the tails of the high-speed streams, and
in the low-speed streams between the high-speed streams.
CMEs were strongly compressed by high-speed streams when they were
in front of high-speed streams. 

We found that approximately half of the disturbances were associated with CMEs
even around the solar minimum.
Approximately 20 $\%$ of the geomagnetic disturbances were associated with
both high-speed streams and CMEs.
CMEs controlled the magnitudes of such disturbances while high-speed streams
control the disturbed periods. 
Even around the solar minimum, CMEs seem to make up a large portion
of solar sources of geomagnetic disturbances.

\end{document}

%% End of NOBEYAMA98  ABSTRACT.