%%
%%                     NOBEYAMA98  ABSTRACT
%%
%%                  Deadline: September 5, 1998
%%
%%        Please send by E-MAIL to nbym98@solar.nro.nao.ac.jp.
%%

\documentstyle{article}
\textwidth 15 cm
\oddsidemargin 1 cm
\evensidemargin 1 cm
\textheight 24 cm
\topmargin 0 cm
\begin{document}

%% TITLE

\begin{center}
{\large\bf {" Mm-Wave Diagnostics of Electric Currents
in  Magnetic Loops".}}
\end{center}

%% AUTHORS


\begin{center}
{\bf {V.Zaitsev$^{1}$, A.Stepanov$^{2}$, S.Urpo$^{3}$ and
S.Pohjolainen$^{3}$}}
\end{center}

%% INSTITUTIONS

\begin{center}
$^1$ {Institute of Applied Physics RAS, Nizhny Novgorod, Russia} \\
$^2$ {Pulkovo Observatory RAS, S.-Petersburg, Russia} \\
$^3$ {Metsahovi Radio Observatory, Helsinki Univ. of
Technology, Espoo, Finland}\\
\end{center}

A method of estimating the electric currents in coronal magnetic
field is proposed. The method is based on representing a
current-carrying arch by an equivalent LRC circuit and analyzing
high-Q modulations of the mm-wavelength emission during solar flares.
The electric current is assumed to be generated by converging streams
of photospheric material and to flow along the coronal part of the
loop from one foot to the other, closing in the subphotospheric
layers. An equation for the equivalent LRC circuit is obtained, in
which the capacitance and resistance depend on the current. Analysis
of the mm-wavelength data for sixteen flares recorded at the
Metsahovi Radio Observatory reveals modulation periods from 0.7--17s,
which imply current values \mbox {$I=(6\times10^{10}-1.4\times
10^{12})$ A}.  Comparison of the current energy stored in the circuit
with the thermal energy for two flare events indicates that only
about 5\% of the energy of the electric circuit is released in the
flare. This suggests that the influence of the flare energy release
on the coronal magnetic structure is small. The events studied showed
a tendency for the energy release to decrease when the current is
increased.  This can be understood in terms of plasma parameters
beta, which decreases when the current grows, lowering the
probability that the instabilities responsible for flares will
develop.
\end{document}