%%
%%                     NOBEYAMA98  ABSTRACT
%%
%%                  Deadline: September 5, 1998
%%
%%        Please send by E-MAIL to nbym98@solar.nro.nao.ac.jp.
%%

\documentstyle{article}
\textwidth 15 cm
\oddsidemargin 1 cm
\evensidemargin 1 cm
\textheight 24 cm
\topmargin 0 cm
\begin{document}

%% TITLE

\begin{center}
{\large\bf {Magnetic Field Diagnostics in the Low Corona from Microwave
Circular Polarization Inversion}}
\end{center}

%% AUTHORS

\begin{center}
{\bf {C. E. Alissandrakis}}
\end{center}

%% INSTITUTIONS

\begin{center}
{Secction of Astro-Geophysics, Department of Physics, University of
Ioannina, Greece}\\
\end{center}

%% ABSTRACT

 % Please write your abstract here. Size limit is one page (15 cm x 24 cm)
 % with 10pt font size. Please avoid to use figures and to use \new...
 % and \renew... commands.

The characteristics of polarization of the radio emission are determined by
the emission mechanism and by the propagation conditions in the corona. In
the case of weak coupling between the two electromagnetic wave modes, the
polarization changes along the ray path, reflecting the local physical
conditions; this results in inversion of the sense of circular polarization
when a transeverse field region (TFR) is crossed. On the contrary, if the
wave coupling is strong, the polarization is fixed and its sense does not
change when a TFR is crossed. As a result, Stokes $V$ maps of active regions
do not always correspond to the magnetic polarities shown in photospheric
magnetograms. The differeces depend on the wavelength, the heliographic
position of the region, as well as on the density and the magnetic field of
the corona, at about 0.1 $R_\odot$ above the photosphere.

In this short review I will present older and recent observation of
polarization inversion and will discuss the diagnostics they provide on the
magnetic field.

\end{document}

%% End of NOBEYAMA98  ABSTRACT.