%%
%%                     NOBEYAMA98  ABSTRACT 
%%
%%                  Deadline: September 5, 1998
%%  
%%        Please send by E-MAIL to nbym98@solar.nro.nao.ac.jp.
%% 

\documentstyle{article}

\textwidth 15 cm
\oddsidemargin 1 cm
\evensidemargin 1 cm
\textheight 24 cm
\topmargin 0 cm
%% \input tcilatex

\begin{document}


\begin{center}
{\large {\bf Temporal behaviour of the circular polarization\\ of solar
bursts at 7 GHz }}
\end{center}
\begin{center}
{\bf {E. Correia and P. Kaufmann }}
\end{center}
\begin{center}
{Centro de Radio Astronomia e Aplicacoes Espaciais - CRAAE } \\ {Instituto
Presbiteriano Mackenzie, Rua da Consolacao 896, 01302-000, Sao Paulo, Brazil}%
\\
\end{center}

We present the results of the circular polarization degree variations in
association to the fluxes of bursts observed at 7 GHz. The observations were
performed by a 1.5 m antenna patrol polarimeter, recently renewed, achieving
good sensitivity ($<$ 0.5 sfu) and 20 ms time resolution. The 7 analysed
events are essentially small and impulsive (peak flux below 30 sfu). The
analysis of the variation of the polarization degree in association to the
flux showed that the polarization could be separated in two components. One
slow component with a degree of 5 - 30 \%, already defined just in the
beginning of the event, presenting a stationary behaviour or an increasing
one during the event evolution. The events presenting no structure in their
time profiles were classified as simple, and the events presenting fast
structures are classified as complex. The analysis of the time variations of
the polarization degree and flux of simple events suggests that in some
cases there are correlated structures, but the results are not conclusive.
It is necessary to study a larger number of events. The complex events
present fast time variations in polarization degree and flux, suggesting a
correlation in phase or in anti-phase with the flux. The amplitude of the
fast variations in polarization for the weak events (flux below 30 sfu) was
about 15\%, while for a strong one ($>$ 1000 sfu) was only 2\%. The V Stokes
parameters for these complex events, are almost the same (6 sfu),
independently of the intensity (I). If this behaviour could be confirmed for
a large collection of events, this might mean that the emergent radiation
from the bursts have a well defined V polarized component, while the degree
of polarization becomes negligible in strong bursts, since the I parameter
is too large compared to V. This finding confirms earlier results showing
that the small bursts tend to have higher polarization degrees.

\end{document}