%%
%%                     NOBEYAMA98  ABSTRACT-2
%%
%%                  Deadline: September 5, 1998
%%
%%        Please send by E-MAIL to nbym98@solar.nro.nao.ac.jp.
%%

\documentstyle{article}
\textwidth 15 cm
\oddsidemargin 1 cm
\evensidemargin 1 cm
\textheight 24 cm
\topmargin 0 cm
\begin{document}

%% TITLE

\begin{center}
{\large\bf { A  Broadband Radiospectrometer and Preliminary Results }}
\end{center}

%% AUTHORS

\begin{center}
{\bf {QiJun Fu$^{1}$ Yuying Liu$^{1}$ Huirong Ji$^{1}$ and Guangli 
Huang$^{2}$ }}
\end{center}

%% INSTITUTIONS

\begin{center}
$^1$ {Beijing Astronomical Observatory, Chinese Academy of Sciences, 
Beijing 100012, P.R. China} \\
$^2$ {Purple Mountain Observatory, Chinese Academy of Sceinces, 
Nanjing 210008, P.R. China} \\
\end{center}

%% ABSTRACT

 % Please write your abstract here. Size limit is one page (15 cm x 24cm)
 % with 10pt font size. Please avoid to use figures and to use \new...
 % and \renew... commands.

                            

       The radio spectrometer has become an efficient tool for the study of 
     physical process in the solar corona. Apart from the classic large-scale 
     spectral types of solar radio bursts, a wealth of fine structures(FS) 
     have been detected, opening a rich field for the study of energy 
     fragmentation in flare and flare-like processes, the examination of 
     flare dynamics, and applying plasma physics.

     Microwave spike bursts are one of the microwave FS, they are believed
     to be produced by electron cyclotron maser(ECM) in magnetic loops. 
     Recently, microwave type III bursts, which are rapid drifting microwave
     FS in the range of more than 3000 MHz/s were discovered. They are 
     possibly the signatures of travelling electron beams in the solar 
     atmosphere. The exact emission mechanism for these phenomena, in 
     particular the source configuration , the plasma parameters and 
     the distribution of radiating electrons are not clear. For a detailed
     study of these problems new observation of intensity and polarization
     with high resolution in time and in frequency in decimeter and 
     microwave wavebands are essential. In order to investigate these 
     features in great detail, spectrometer with high temporal and spectral
     resolution are being developed by the solar radio astronomy community
     of China(Beijing Astronomical Observatory(BAO), Purple Mountain 
     Observatory(PMO), Yunnan Astronomical Observatory(YAO), and Nanjing 
     University(NJU)) (Fu, et al. 1995 Solar Phys.160,97). The frequency range 
     from 0.7-7.6 GHz is covered by five spectrometers in frequency ranges 
     of 0.7-1.4 GHz, 1.0-2.0 GHz, 2.6-3.8 GHz, 4.0-5.2 GHz, and 5.2-7.6 GHz,
     respectively. The radiospectrometers form a comined type of multi-channel 
     and swept-frequency receiving system. The main characteristics of the 
     spectrometers are: frequency resolution: 1-10 MHz; temporal resolution:
     1-10 ms; sensitivity: better than 2% of the quiet Sun level. We pay 
     special attention to the sensitivity and the accuracy of polarization. 
     Now, the 2.6-3.8 GHz and 1.0-2.0 GHz(50 ms) spectrometers has come 
     into operation since the end of September, 1996 and January, 1994, 
     respectively. The whole broadband radiospectrometer will be set up in 
     1999. Some interesting and peculiar results have been obtained, 
     including: Microwave TypeIII burst pair (Fu, et al. 1997 Acta 
     Astrophysica Sinica 17, 441); A pair of spike bursts(Fu, et al. 1998,
     submitted to ApJ L); Mini-Type-U bursts; millisecond quasi-periodic 
     pulsation group; and so on.
 
\end{document}

%% End of NOBEYAMA98  ABSTRACT.