%%
%%                     NOBEYAMA98  ABSTRACT
%%
%%                  Deadline: September 5, 1998
%%
%%        Please send by E-MAIL to nbym98@solar.nro.nao.ac.jp.
%%

\documentstyle{article}
\textwidth 15 cm
\oddsidemargin 1 cm
\evensidemargin 1 cm
\textheight 24 cm
\topmargin 0 cm
\begin{document}

%% TITLE

\begin{center}
{\large\bf { SRBL - Solar Radio Burst Locator }}
\end{center}

%% AUTHORS

\begin{center}
{\bf {G. J. Hurford, B. L. Dougherty, W. B. Freely and H. Zirin }}
\end{center}

%% INSTITUTIONS

\begin{center}
{Caltech, Solar Astronomy 264-33, Pasadena, CA 91125, USA}
\end{center}

%% ABSTRACT

The position of flares on the solar disk is an important factor for the
prediction of solar-terrestrial activity.  Since such information is
not always available, the Solar Radio Burst Locator (SRBL) was
developed at Caltech as an all-weather system to locate microwave
bursts on the solar disk and to provide information on their spectra
and intensity.  Each fully automated system uses a single 1.8 meter
diameter antenna with an az-el mount and a frequency-agile receiver to
monitor the sun at over 100 frequencies between 245 and 18000 MHz.  In
addition to providing burst locations, the output of SRBL can be viewed
either as a dynamic spectrum, a set of light curves or as a sequence of
high-resolution, well-calibrated burst spectra.  Prototype systems have
been in use at the Palehua Solar Observatory in Hawaii and at the Owens
Valley Radio Observatory since 1994.  Production versions of SRBL will
be deployed worldwide in time for MAX-2000 as part of the Solar
Electro-Optical Network (SEON) operated by the US Air Force.  The
resulting data are expected to be available to the scientific
community.  Such a database, with its continuous 24-hour solar
coverage, should prove particularly valuable for statistical studies
and as a reliable source of ancillary data in support of other solar
burst observations.  This poster will describe the SRBL design,
calibration, status and performance to date.


\end{document}

%% End of NOBEYAMA98  ABSTRACT.